## Slide 1: Carbon Fiber Frames
5-foil stack
Carbon fiber frame
Mechanical support structures are outer frames with windows (e.g. aluminized mylar foil, not shown here) instead of solid PCBs to reduce radiation length in the active area
Frames are made from carbon fiber composites that have high strength to take up the tension from the stretched foils
Exploded assembly view
Assembled detector
Carbon fiber frames
5-foil stack
Gas seal frame

## Slide 2: CF Composite R&D
Trimmed quarter-frame (test piece, 175 g)
Raw full drift frame before trimming
Carbon Fiber Composite:
Araldite epoxy (AY103)
Intermediate-modulus uni-directional
carbon fiber (“IM7”)
8 layers
Produced in-house